## Slide 1: Health Hazards
Special Emphasis Program
Presented by:
Notes: Revised 12/2021
The information in this presentation is provided voluntarily by the N.C. Department of Labor, Education Training and Technical Assistance Bureau as a public service and is made available in good faith. This presentation is designed to assist trainers conducting OSHA outreach training for workers. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
The information and advice provided on this Site and on Linked Sites is provided solely on the basis that users will be responsible for making their own assessment of the matters discussed herein and are advised to verify all relevant representations, statements, and information.
This presentation is not a substitute for any of the provisions of the Occupational Safety and Health Act of North Carolina or for any standards issued by the N.C. Department of Labor. Mention of trade names, commercial products, or organizations does not imply endorsement by the N.C. Department of Labor.

## Slide 2: Objectives
After this course, students will be able to:
  Understand the NCDOL Health Hazards Special Emphasis Program (SEP) requirements for:
    Lead
    Asbestos
    Hexavalent chromium (CrVI)
    Isocyanates
    Silica
  Recognize exposure effects, health effects and abatement methods for each

## Slide 3: Health Hazards SEP
Overexposures to these chemicals can lead to serious health effects.
OSH Division has increased the number of inspections to focus on industries that use these chemicals and substances.

## Slide 4
Health Hazards SEP
Lead
29 CFR 1910.1025
29 CFR 1926.62

## Slide 5: Lead Standard
1910.1025
1926.62
Means metallic lead, all inorganic lead compounds, and organic lead soaps
  Excluded from this definition are all other organic lead compounds.
Exposure sources
  Lead-based paint, batteries, battery recycling, foundries, welding/cutting and brazing
  Lead shot, indoor/outdoor shooting ranges

## Slide 6: Lead Health Effects
Acute effects: Show up sooner usually after high exposure.
  Symptoms can include metallic taste, stomach pain, vomiting, diarrhea and black stools which could potentially cause intoxication, coma, respiratory arrest, or death.
  Short term occupational exposures of this magnitude are highly unusual, but not impossible.
1910.1025, Appendix A
1926.62, Appendix A

## Slide 7: Lead Health Effects
Chronic effects: Take longer to develop and often are attributed to lower cumulative exposures over time.
  Symptoms can include tiredness, weakness, weight loss, insomnia, headache, nervous irritability, fine tremors, numbness, dizziness, anxiety and hyperactivity which could potentially lead to:
    Damage of the nervous system and brain
    Anemia
    Kidney disease
1910.1025, Appendix A
1926.62, Appendix A

## Slide 8: Lead Exposure Limits
Permissible exposure limit (PEL) = 50 µg/m³ as an 8-hour time-weighted average (TWA)
  Employers shall implement engineering controls and safe work practices to prevent exposure
  Employers shall provide protective clothing and where necessary, and respiratory protection in accordance with 29 CFR 1910.134
Action level (AL) = 30 µg/m³ as an 8-hour TWA
1910.1025
1926.62

## Slide 9: Medical Surveillance
In General Industry, employer shall institute a medical surveillance program for employees who are or may be exposed above the action level for more than 30 days per year.
  Appendix C - Medical Surveillance Guidelines
In Construction, employer shall provide initial medical surveillance for any employee exposed at or above the action level for any one day.
1910.1025
1926.62

## Slide 10: Hierarchy of Controls
1910.1025
1926.62

## Slide 11: Abatement Methods
Elimination
Substitution
Engineering controls
  Mechanical ventilation
  Isolation
Administrative controls
  Housekeeping
  Personal hygiene practices
  Designated break areas
Personal protective equipment (PPE)
  Respiratory protection
  Protective work clothing
1910.1025
1926.62

## Slide 12
Health Hazards SEP
Asbestos
29 CFR 1910.1001
29 CFR 1926.1101

## Slide 13: Asbestos
A group of naturally occurring fibrous silicate minerals with useful properties such as thermal insulation, chemical and thermal stability, and high tensile strength.
Used in building materials for resistance against heat and corrosion.
Asbestos includes:
  Chrysotile
  Amosite
  Anthophyllite
  Actinolite
1910.1001
1926.1101
Nova Development
  Crocidolite
  Tremolite
Notes: 13

## Slide 14: Asbestos
Airborne fibers range from 5 µm or greater, with a length-to-diameter ratio of at least 3 to 1.
1910.1001
1926.1101
Notes: 14

## Slide 15: Asbestos
ACM: “Asbestos-containing material,” any material containing >1% asbestos.
PACM: “Presumed asbestos-containing material” – thermal system insulation and surfacing material found in buildings constructed no later than 1980.
1910.1001
1926.1101
Notes: 15

## Slide 16: Health Effects
Asbestos particles are breathed into the smallest part of the lungs causing permanent scarring, stiffening and damaging your lungs.

## Slide 17: Asbestos Health Effects
Asbestosis: A serious, progressive, long-term non-cancer disease of the lungs.
Lung Cancer: Causes the largest number of deaths related to asbestos exposure.
  Most common symptoms of lung cancer are coughing and a change in breathing.
Mesothelioma: A rare form of cancer found in the thin lining (membrane) of the lung, chest, abdomen, and heart.
  Most cases are linked to asbestos exposures.
1910.1001
1926.1101
Notes: 17

## Slide 18: Exposure Limits
1910.1001
1926.1101
Permissible exposure limit
  0.1 fiber per cubic centimeter (f/cc) of air as an 8-hour TWA.
Excursion limit
  Not more than 1 f/cc averaged over 30 minutes.
Monitoring
  Initially for workers who are or may be exposed at or above the PEL and/or above the excursion limit.
  Periodic if above PEL or excursion limit.

## Slide 19: Responsibility
Building/facility owner
Removal/abatement of asbestos is covered by 29 CFR 1926 (Construction)
Must adhere to:
  Multi-employer worksite
    Hazards abated by contractor who created.
    Inform others of measures to control exposures.
    Adjacent employer will check containment.
    General contractor (GC) requires compliance.
  Competent person
1910.1001
1926.1101
Notes: 19

## Slide 20: Medical Surveillance
Required when above PEL/excursion limit
  Pre-placement examinations
    Medical/work history
    Complete physical exam with emphasis on respiratory system, cardiovascular system and digestive tract
    Completion of questionnaire – Appendix D
    Chest X-Ray (Roentgenogram)
    Pulmonary function test (PFT)
    Any additional tests required by the Physician
    or other Licensed Healthcare Professional (PLHCP)
  Periodic exam (annually)
  Upon termination of employment (1910)
1910.1001
1926.1101

## Slide 21: Respirator Selection
1910.1001
1926.1101
When is respiratory protection required?
  Above PEL
  Based on Class of work performed
Provided in accordance with 29 CFR 1910.134 (b) - (d) (except (d)(1)(iii)), and (f) - (m)
  Proper selection per 29 CFR 1910 or 29 CFR 1926
  High efficiency particulate air (HEPA) filters for all air purifying respirators (APR)
  No filtering face pieces (dust masks)

## Slide 22: Abatement
Elimination
Substitution
Engineering controls
  Mechanical ventilation
Administrative controls
  Procedures
  Housekeeping
  Hygiene facilities
PPE
  Respiratory protection
  Protective work clothing
1910.1001
1926.1101

## Slide 23
Health Hazards SEP
Hexavalent Chromium
29 CFR 1910.1026
29 CFR 1926.1126

## Slide 24: Hexavalent Chromium
Toxic form of chromium metal that is generally man-made.
Used in many industrial applications primarily for its anti-corrosive properties.
Can be created during certain “hot work” processes where the original form of chromium was not hexavalent.
1910.1026
1926.1126
Notes: 24

## Slide 25: Examples of Cr(VI) Compounds
Ammonium dichromate
Calcium chromate
Chromium trioxide or chromic acid
Lead chromate (chromium yellow)
Potassium chromate
Potassium dichromate
Sodium chromate
Strontium chromate
Zinc chromate
(NH4)2Cr2O7
CaCrO4
CrO3
PbCrO4
K2CrO4
K2Cr2O7
Na2CrO4
SrCrO4
ZnCrO4
1910.1026
1926.1126
Notes: 25

## Slide 26: Affected Operations
  Electroplating
  Welding on stainless steel or Cr(VI) painted surfaces
  Painting
    Aerospace
    Auto body repair
  Chromate pigment and chemical production
  Chromium dye and catalyst production
  Glass manufacturing
  Plastic colorant production
  Construction
  Refractory brick restoration
  Paint removal from bridges
  Traffic painting
1910.1026
1926.1126
Notes: 26

## Slide 27: Health Effects
Lung cancer (via inhalation of Cr(VI)
Irritation or damage to the nose, throat, and lung (respiratory tract) at high levels
Irritation or damage to the eyes and skin if contact at high concentrations
1910.1026
1926.1126
“Chrome Hole” – Employee was chrome plating small appliance parts

## Slide 28: Major Provisions
  Scope
  Permissible exposure limit
  Exposure determination
  Recordkeeping
  Methods of compliance
  Respiratory protection
  Protective work clothing
  and equipment
  *General Industry only
  Hygiene areas and practices
  Medical surveillance dates
  Communication of hazards
  Regulated areas*
  Housekeeping*
1910.1026
1926.1126
Notes: 28

## Slide 29: Exposure Limits
Permissible exposure limit
  5 µg/m3, calculated as an 8-hour time-weighted average
Action level
  2.5 µg/m3
Exposure determination
  See paragraph (d) for more specifics
1910.1026
1926.1126

## Slide 30: Monitoring
Scheduled
  Initial monitoring indicates exposures are:
    Below the AL: monitoring can be discontinued
    At or above the AL: monitor every 6 months
    Above the PEL: monitor every 3 months
  Periodic personal monitoring
Performance-oriented option
  To determine 8-hour TWA for each employee
  based on any combination of the following:
    Air-monitoring data
    Historical monitoring data
    Objective data
1910.1026
1926.1126

## Slide 31: Regulated Areas
General Industry employers only
  Areas where exposures exceed or can be reasonably expected to exceed the PEL.
    Must be demarcated from other areas.
    Must limit access to employees who have a need to be there.
1910.1026(e)

## Slide 32: Medical Surveillance
Occupationally exposed for 30 days or more at or above the AL
Conducted within 30 days after initial assignment or exposure of uncontrolled release
Within 30 days after PLHCP written medical opinion
Employee shows signs and symptoms of adverse health effects or signs and symptoms of exposure
Termination of employee
Annually
1910.1026
1926.1126

## Slide 33: Abatement
Elimination
Substitution
Engineering controls
  Mechanical ventilation
Administrative controls
  Housekeeping
  Hygiene facilities
  Regulated areas of work
PPE
  Respiratory protection
  Protective work clothing
1910.1026
1926.1126

## Slide 34
Health Hazards SEP
Isocyanates
29 CFR 1910.1000
29 CFR 1926.55

## Slide 35: Isocyanates
Compounds containing the isocyanate group
(-NCO)
  React with compounds containing alcohol (hydroxyl) groups to produce polyurethane polymers, which are components of polyurethane foams, thermoplastic elastomers, spandex fibers, and polyurethane paints.
1910.1000
1926.55
NCDOL Photo Library

## Slide 36: Isocyanates
Isocyanates can also be found in raw materials that make up all polyurethane products.
PELs/Threshold Limit Values (TLV), are very low (<1 ppm).
1910.1000
1926.55
NCDOL Photo Library

## Slide 37: Health Effects
Health effects of isocyanate exposure include irritation of skin and mucous membranes, chest tightness, and difficult breathing.
  Isocyanates include compounds classified as potential human carcinogens and are known to cause cancer in animals.
Main effects of hazardous exposures are occupational asthma and other lung problems, as well as irritation of the eyes, nose, throat, and skin.
1910.1000
1926.55

## Slide 38: Medical Surveillance
It is recommended that workers exposed
to isocyanates at or above the PEL or TLV undergo annual medical examinations and health surveillance under the supervision of a PLHCP.
Physical examination should detail the workers demographic and occupational history.
A pulmonary function test (spirometry) is recommended as well as a blood sample to monitor the systemic effects.
1910.1000
1926.55

## Slide 39: Abatement
Elimination
Substitution
Engineering controls
  Mechanical ventilation
Administrative controls
  Housekeeping
  Personal hygiene
  Regulated areas of work
PPE
  Respiratory protection
  Protective work clothing
1910.1000
1926.55

## Slide 40
Health Hazards SEP
Silica
29 CFR 1910.1053
29 CFR 1926.1153

## Slide 41: Silica
Silicosis, an irreversible but preventable disease, is the illness most closely associated with occupational exposure to the material, which also is known as silica dust.
1910.1053
1926.1153

## Slide 42: Silica
If employer only suspects that silica is a hazard at the workplace, employer is still required to communicate this potential hazard to all employees.
Examples include:
  Abrasive blasting
  Blast furnaces
  Cement manufacturing
  Ceramics, clay, and pottery
1910.1053
1926.1153
NCDOL Photo Library

## Slide 43: Silica
  Concrete mixing
  Demolition
  Electronics industry
  Foundry industry: grinding, molding, shakeout, core room (high risk)
  Hand molding, casting, and forming
  Jack hammer operations
  Manufacturing abrasives, paints, soaps, and glass
  Mining
  Rolling and finishing mills
  Sandblasting
  Setting, laying, and repairing railroad track
1910.1053
1926.1153

## Slide 44: Health Effects
Occupational exposure to respirable crystalline silica is associated with the development of silicosis, lung cancer, pulmonary tuberculosis, and airway diseases.
  Exposures may also be related to the development of autoimmune disorders, chronic renal disease, and other adverse health effects.
1910.1053
1926.1153
USDOL Photo Archive

## Slide 45: Silica Exposure Limits
AL = 25 µg/m³ as an 8-hour TWA
  Written Exposure Control Plan (ECP)
PEL = 50 µg/m³ as an 8-hour TWA
  Employers must use engineering controls to prevent or reduce exposure
  Respiratory protection is required when exposure remains above PEL after engineering controls are utilized or when required by Table 1.
1910.1053
1926.1153

## Slide 46: Medical Surveillance
At no cost to the employee.
At a reasonable time and place.
General Industry
  When exposed at or above 25 µg/m3 for 30 or more days for any 12 consecutive months.
Construction
  When employee is required to wear a respirator 30 or more days for any 12 consecutive months.
1910.1053
1926.1153

## Slide 47: Specific Control Methods
1926.1153(c)(1)
In Construction
  Table 1
    18 specific tasks
    Identifies specific engineering controls to use
      Water delivery systems
      Dust collection systems
    Fully and properly implemented controls listed
      Do not have to comply with PEL
      Do not have to conduct exposure assessment

## Slide 48: Table 1 - Example
Equipment/Task | Engineering and work practice control methods | Required respiratory protection and minimum assigned protection factor (APF) | 
 |  | ≤ 4 hours/shift | >4 hours/shift
Handheld power saws (any blade diameter) | Use saw equipped with integrated water delivery system that continuously feeds water to the blade Operate and maintain tool in accordance with manufacturer's instructions to minimize dust emissions: |  | 
 | When used outdoors | None | APF 10
 | When used indoors or in an enclosed area | APF 10 | APF 10
1926.1153(c)(1)

## Slide 49: Abatement
Elimination
Substitution
Engineering controls
  Mechanical ventilation
Administrative controls
  Housekeeping
  Personal hygiene
  Regulated areas of work
PPE
  Respiratory protection
  Protective work clothing
1910.1053
1926.1153

## Slide 50: Summary
In this course, we discussed the following:
  NCDOL Health Hazards Special Emphasis Program for:
    Lead
    Asbestos
    Hexavalent chromium (CrVI)
    Isocyanates
    Silica
  Exposures, health effects and abatement methods for each

## Slide 51: Thank You For Attending!
Final Questions?